## Slide 1: 08 – Branches, Commits and Upstreaming
COMP 190 – Dickinson College
Fall 2021
Images from:
https://git-scm.com/downloads/logos
https://github.com/logos
https://www.youtube.com/watch?v=Tyd0FO0tko8
Notes: Today will be a quick overview of where you are after the last activity
And how you go from there to upstreaming contributions.
We’ll look at a prototypical way that this happens
But recognize that there are lots of variants that you may encounter if you work on other projects.

## Slide 2: GitHub and git: Fork and Clone
The
Upstream
Repository
Your
Origin
Repository
Your
Local
Repository
Notes: This is your current state after completing A07.
ASK: Names for each of the different repos.
- Upstream
- Origin
- Local
Notes:
- These terms are conventions – some use different terms.
- They are also relative to the project.
- You will have a local for each project
- That local will have its own origin.
- It is the origin, because that's where the local was cloned from.

## Slide 3: GitHub and git: Make Changes*
Simplified
for now
Notes: You claimed an issue that needs to be fixed in FarmData2.
So you are ready to make some changes.
Last time we said this was a simplified view.
- that making changes was a little more complicated than just editing the files.
- the reason it is more complicated is that we are using version control
- Recall that version control requires that we keep a history of all changes.
- That adds some overhead
- But provides benefits.
Today we’ll see the details of how that works.

## Slide 4: git: Branches and Commits
Time
main
Branch: A branch is a named sequence of commits.
Commit: Each commit describes a set of changes to the project.
  The changes made.
  Who made them.
  When they were made.
  A unique identifier.
Commits
Tip: Can also think of a commit as
a copy of all the files
in the repo at a given point in time.
Notes: To understand how changes are made and upstreamed
We need to know about branches and commits.
The contents of a repository are organized into branches.
A Branch is a named sequence of commits.
We often represent branches and commits using
- a line for the branch
- a dot for each commits
A commit describes a set to changes.
- includes the changes, who, when, and an Id.
Think of this sort of like track changes in Word or Google Docs if you have used that.
Branches grow over time:
- Developers add new features, fix bugs, revise code, delete unused things, etc.
- Each change is described by a new commit that becomes part of the branch.
It is this sequence of commits that documents the history of the project.
- Technically, the way it works is to start from an empty project and apply each commit.
- When you get to the end you have the current state of the project.
TIP: It is often easier to just think of every commit as its own full copy of the files at that point in time.
- Note: Because each commit has a unique identifier it is possible to reset the project to any commit.
- Useful for
- understanding changes
- undoing undesirable changes

## Slide 5: git: Main and Feature Branches
Time
main
main Branch: the designated starting point for new work.
feature Branch: a copy of the main branch on which a new feature, bug fix, or other changes are made.
newColorScheme
newColorScheme2
nullPointerFix
RULE: Only commit to feature branches. Maintainers will merge accepted changes into the main branch.
Notes: Repositories will usually have multiple branches.
One branch in the upstream project will be designated as the point from which new work should begin
- This branch is often called the main branch.
- also likely to see it called:
- the master branch – outdated terminology
- the dev branch indicating its where new development is occurring.
- there is nothing special about the name – it is just a convention.
When you want to do some work (add a feature, fix a bug, etc)
- you create a new branch
- the new branch is like a full copy of the repository.
- you then add commits for the work you want to do to the new branch.
- these branches on which you do work are generically called feature branches.
- but you will give them specific names that are descriptive of what they do.
- e.g. newColorScheme – to develop a new color scheme for the user interface.
You may be working on multiple different tasks at the same time.
- When doing so you can have multiple feature branches simultaneously.
- e.g. stop working on the new color scheme to fix a null pointer exception that was discovered.
- You can even make a branch of a branch.
- e.g. started working on the new color scheme
- but after a while decided you wanted to try it a different way.
- instead of deleting what you’ve done
- you can go back and create a new branch from any commit and try something different.
- that way if you later decide the first way actually was better you can jump right back to it.
- You can switch back and forth between branches to
- work on different tasks
- to try different approaches
RULE: You should only ever make commits to feature branches.
- the maintainers will respond to pull requests
- if they accept your changes
- then they will merge them into to the main branch

## Slide 6: GitHub and git: Repos and Branches
Notes: So let’s now see how the idea of branches translates into work with GitHub and git.
- we’ll do it conceptually here
- Then you’ll do it hands on in the rest of the class period
- and again for homework.
When you fork and clone a repository you get a copy of its branches,
Which includes all of the commits and all of the history as well.
So this a more accurate picture of where you are.
Your origin and local clone repos contain the main branch and its commits from the upstream.

## Slide 7: git: Branch/Repo vs Local Files
Tip: Think of your local files as a copy of the last commit.
Notes: So now you have your local repository.
- it contains the branches copied from the upstream
- but the commits in there are fixed
- they are part of the project history
- so you can’t change them.
Instead, what happens is that you have a yet another copy called your local files.
- You saw these in the last activity.
- When you changed into the repository directory and looked at the files (ls)
- You should have noticed that they look exactly the same as what is in the repo.
- That is because they are essentially a copy of the last commit in the repo.
- Now, because the local files are a copy, and not a commit
- you can change them.
- so as you work you are making changes to your local files.
- the commits in the repository (i.e. the history) do not change.
Tip: Think of your local files as a copy of the last commit
- at least until you change them.

## Slide 8: git: Create and Switch to Feature Branch
Switching to a feature branch makes it the target for new commits.
Notes: As said earlier – as a RULE you will not work on code in the main branch.
Instead
- you will create a new feature branch in your local repo
- you then switch to that feature branch.
- switching to a feature branch makes it the target for future commits.
Note: there are no commits in the feature branch yet
- It is just a copy of the main branch at this point.
- when you change the local files you will make commits
- those commits will go onto the feature branch because we switched to it.

## Slide 9: Local Files: Edit Local Files
Notes: Now when you edit your local files
- they will be become different from the last commit
- note that the commit didn’t change.

## Slide 10: git: Stage Changes and Commit
ProTip: Each commit should contain a nameable unit of work.
Notes: When you have some unit of work done
- You need to commit it to the feature branch.
This is a two step process:
- First you add the files that you have changed to the Staging area
- Then you commit those changes to the feature branch.
Why two steps?
- ProTip: Commits should be nameable units of work.
- they should hang together in some way.
- So you may end up making a bunch of changes
- They may logically be multiple nameable changes.
- You could stage and commit one of the changes
- Then do the other.
- That way each change has it own record in the project history.

## Slide 11: git: Edit/Add/Commit Cycle
ProTip: If It takes multiple nameable units of work to complete a feature or bug fix. Give each its own commit.
Notes: Can repeat the edit, add, commit cycle.

## Slide 12: GitHub and git: Push Branch to Origin
Notes: Now in order to upstream
- you need to get your changes into the cloud.
- so that the upstream can see them
To do that
- you push your branch to your origin.

## Slide 13: GitHub: Make Pull Request
A Pull Request asks the maintainers to consider merging your changes into the main branch.
Notes: Once your branch is in the cloud
- you can notify the upstream of your changes
- ask them to consider merging them into main branch.
This is the Pull Request

## Slide 14: What’s Next?
A08/Q08 – 1 week – Extra essential!
Revise and resubmits
Reading for discussion
Notes: By the end of A08 you will have made a PR to the upstream.
Next class we’ll see how the project maintainers merge those requests
And then what you as a contributor do next.
Then you’ll repeat the process for practice
And we’ll see some of the issues that arise when many developers are working asynchronously.

## Slide 15: Acknowledgments:
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
https://creativecommons.org/licenses/by-nc/4.0/